# Table of Contents

# Cartesian/Polar Grid Pattern Matching
Options:
1. Search parameter space of (grid line count, grid line start, grid line number, angle) for X and Y separately, while performing fast cross correlations using FFTW3.
2. Scan the X histogram vertically from top to bottom, and stopping when the existing points no longer fit the pattern FOREGROUND = START + (I – 1) * STEP

Option 1 took very long (30 seconds) to perform X then Y searches. Like most global peak searches, there were plenty of local peaks to interfere with performing gradient, and other, search optimizations.
Conclusion – Careful examination of various polar plots shows that the use of concentric rings as gridlines has little correlation with the plot type in terms of cartesian or polar. So cartesian/polar plot identification coding was stopped, and the files put into the deprecated subdirectory.
# Tutorial Video
Originally the tutorial video was to be added to the qrc file, but that caused a segfault on a 9MB file. Google search revealed adding large multimedia file(s) to resource file causes problems (since data gets stored as C array, and there are swap issues).
An attempt was made to play the mp4 file using Qt, by appending “multimedia multimediaplugins” to QT in the project file. This failed with an error that should have been fixed by installing libgstreamers. Playback using Qt was abandoned as too complicated and fragile to try to implement on many different platforms.
## Help Engine
1. Installed qttools5-dev and qttools-dev-tools in muon
2. 'build' script in help subdirectory builds the help files for the engauge executable. If the help files are not built, selecting Help / Help menu option brings up an empty Help dialog.
## JPEG2000
## Plugin qtjp2imageformat
Downloaded from https://github.com/kbinani/qt-solutions. Code is from qt3 and unmaintained. This requires the JasPer library, which according to https://en.wikipedia.org/wiki/JPEG_2000 has limited JPEG2000 feature support.
## OpenJPEG
Self-contained library with attractive licensing.
# FFTW Build
Building fftw 3.3.3:
./configure --prefix=$HOME/fftw-3.3.3 –enable-shared CFLAGS=”-fPIC”
# Poppler Build
Building poppler 0.51.0 with support for qt5 wrapper (=bundling poppler-qt5.h file):
./configure --prefix=$HOME/poppler-0.51.0 CXXFLAGS="-I$HOME/Qt5.8/5.8/gcc_64/include -I$HOME/Qt5.8/5.8/gcc_64/include/QtGui" LDFLAGS="-L$HOME/Qt5.8/5.8/gcc_64/lib -L/usr/lib/x86_64-linux-gnu/" LIBS="-lQt5PrintSupport -lQt5Help -lQt5Widgets -lQt5Gui -lQt5Xml -lQt5Core -lpthread"
# Windows Installer
WiX was selected since it is not buggy and is full featured (installs Microsoft products!).
## Guid
Built the following, from https://www.firegiant.com/wix/tutorial/getting-started/the-software-package/, using /cygdrive/C/MinGW/bin/gcc.exe uuidgen.c -lole32:

#define _OLEAUT32_
#include <stdio.h>
#include <unknwn.h>
GUID guid;
WORD* wstrGUID[100];
char strGUID[100];
int count, i;
int main (int argc, char* argv[]) {
  if (argc != 2) {
    fprintf (stderr, "SYNTAX: UUIDGEN <number-of-GUIDs-to-generate>\n");
    return 1;
    }
  count = atoi (argv[1]);
  for (i = 0; i < count; i++) {
    CoCreateGuid (&guid);
    StringFromCLSID (&guid, wstrGUID);
    WideCharToMultiByte (CP_ACP, 0, *wstrGUID, -1, strGUID, MAX_PATH, NULL, NULL);
    printf ("%s\n", strGUID);
    }
  return 0;
}

Results:
Product: {1FBCEF62-3E8D-4E44-A0B5-0F066BAB900D}
Installation package: {4E5846BB-039A-41BF-86EF-2A72B7BEE918}
Exe: {5CE13C36-6B3D-4B6C-B183-C8DC80B70D1F}
Linux Release
1. Download src tarball
2. ./configure –prefix=$HOME/qt-everywhere-opensource-5.5.1 -opensource -release -static -qt-zlib -qt-libpng -qt-libjpeg -qt-xcb -qt-freetype -qt-xkbcommon-x11 -no-opengl
3. make -j 4
4. make install
# Windows Release
## Log4cpp
mkdir build
cd build
cmake -DCMAKE_GENERATOR_PLATFORM=x64 ..
start Visual Studio 15 (2017)
load build/log4cpp.sln
build
# OSX Release
## log4cpp
./configure \
--prefix=/Users/mark/log4cpp CXX=/usr/bin/g++ \
CXXFLAGS="-I/Applications/Xcode.app/Contents/Developer/Platforms/MacOSX.platform/Developer/SDKs/MacOSX10.11.sdk/usr/include -arch x86_64 -Xarch_x86_64 \
-DLOG4CPP_HAVE_SSTREAM"

make
make install
## fftw
 (NOTE THE -enabled-shared!)
./configure \
--prefix=/Users/mark/fftw-3.3.4 \
--enable-shared \
CXX=/Applications/Xcode.app/Contents/Developer/Toolchains/XcodeDefault.xctoolchain/usr/bin/clang++ \
CXXFLAGS="-I/Applications/Xcode.app/Contents/Developer/Platforms/MacOSX.platform/Developer/SDKs/MacOSX10.11.sdk/usr/include"

qmake -config release engauge.pro
## engauge
source dev/osx/macosx_setup
(edit engauge.pro and comment out CONFIG= line)
qmake -config release engauge.pro
(edit engauge.pro and restore CONFIG= line)
make
cp -r bin/documentation engauge.app/Contents/MacOS
## icons
use gimp to create dev/osx/iconset subdirectory
iconutil -c icns digitizer.iconset
cp digitizer.icns engauge-digitizer/engauge.app/Contents/Resources
## deploy
Next step adds libraries to application bundle:

$QT_DIR/bin/macdeployqt engauge.app -dmg
## error message from App Store review
May 15, 2016 at 10:33 AM
From Apple
2.31 - Apps that are not sandboxed appropriately may be rejected
2.31
Your app incorrectly implements sandboxing, or it contains one or more entitlements with invalid values. Please review the included entitlements and sandboxing documentation and resolve this issues before resubmitting a new binary.
com.apple.security.device.usb
False
com.apple.security.assets.pictures.read-write
False
com.apple.security.network.server
False
com.apple.security.temporary-exception.apple-events
False
com.apple.security.device.camera
False
com.apple.security.files.downloads.read-write
False
com.apple.security.files.user-selected.read-only
False
***Value must not be 'false'. If those entitlements are not applicable please remove them.
For information on common app sandboxing issues, please see Technical Q&A QA1773 Common app sandboxing issues.
See App Sandboxing for links to essential video and documentation to learn how to sandbox your application.
As of June 1, 2012, apps must be sandboxed. New apps that are not sandboxed will be rejected. Updates to non-sandboxed apps may be submitted if they only addresses bug fixes and new OS X feature adoption provided that your app was on the Mac App Store prior to June 1st.
Should you need code-level assistance implementing sandboxing, contact Apple Developer Technical Support.
2.31
This app uses one or more entitlements which do not have matching functionality within the app. Apps should have only the minimum set of entitlements necessary for the app to function properly. Please remove all entitlements that are not needed by your app and submit an updated binary for review, including the following:
com.apple.security.assets.pictures.read-only
***The app seems to be opening/saving files using open/savePanel. No direct access to the location(s) was identified.
See App Sandboxing for links to essential video and documentation to learn how to sandbox your application.
Commonly added entitlements that many apps don't need include:
"com.apple.security.network.server"
Apps that initiate outgoing connections (for example, to download new content from your server) only need to include "com.apple.security.network.client". The server entitlement is only necessary for apps that listen for and respond to incoming network connections (such as web or FTP servers).
"com.apple.security.device.usb"
Apps that interact with non-standard USB devices, including HID accessories such as joysticks, may need to include this entitlement. It is not necessary for accessing keyboards, mice, trackpads, printers or external drives such as thumb drives.
Should you need code-level assistance implementing sandboxing, contact Apple Developer Technical Support.

# Static Code Analysis
Run
qmake QMAKE_CXX='scan-build g++'
Build normally
# Translations
## Updating the “To Be Translated” Messages on Transfix
THIS SECTION IS DEPRECATED SINCE ‘AUTO-UPDATE’ SHOULD MEAN TRANSIFEX AUTOMATICALLY LINKS TO https://github.com/markummitchell/engauge-digitizer/blob/master/translations/engauge_en.ts
1. Check to see how many messages are on Transfix by looking for “total strings” in the details for the “source” English translation on Transifex
2. Run ‘lupdate engauge.pro’ and look at translations/engauge_en.ts. The number of ‘<message>’ entries in that xml file equals the number of messages to be translated
3. If there are many more messages listed in engauge_en.ts than on Transifex, it is probably time to update Transifex by continuing with the following steps. Otherwise stop here.
4. In the Transifex tab on the left, click on Resources
5. When ‘engauge_en.ts’ appears, click on it. DO NOT click on ‘Add Resources’
6. Click on ‘Update Source File’
## Downloading translations
Follow the steps in the ‘step_#’ script files in the translations directory
## Deprecated approach
https://wiki.qt.io/How_to_create_a_multi_language_application

1. 'lupdate engauge.pro' safely updates *.ts translation files
2. 'linguist translations/engauge_XX_YY.ts' allows editing of one translation file
3. 'lrelease engauge.pro' builds qm files
4. 'mv translations/*.qm bin/translations'
# R
sudo apt-get install r-base
R
/* Following is from http://www.tutorialspoint.com/r/r_xml_files.htm */
install.packages(“XML”)
library (“XML”)
library (“methods”)
result ← xmlParse (file = “version8_2.dig”)
print (result)
rootnode ← xmlRoot(result)
rootsize ← xmlSize(rootnode)
print (rootsize)

# Windows – Build lib from dll
Lib /def:libfftw3-3.def /OUT:libfftw3-3.lib
# How To Distribute Pre-Releases
1. Go to https://ci.appveyor.com/project/markummitchell/engauge-digitizer/branch/master
2. Select release or debug build
3. Open the artifacts page.
# Boot Knoppix on Mac Mini
1. Plug Windows keyboard into USB socket closest to headphone jack
2. Press Left Alt as system boots
3. Pick boot-up source
4. VboxManage convertdd XXX.ddXXX.vdi - - format VDI - - variant Fixed (on the virtualbox computer)
# Cygport
1. setup-x86_64.exe installations (see also the ‘requires’ line in the .hint file – those entries were listed by cygport at the package-building step):
  1. Libs / libfftw3-devel
  2. Libs / libGL-devel
2. cygport --debug engauge.cygport download
  1. Error ‘ERROR inherit: unknown cygclass qt5-qmake’ occurs when lines in engauge.cygport have \r at the end. Fix is to run ‘unix2dos engauge.cygport’
3. cygport –debug engauge.cygport prep
4. cygport –debug engauge.cygport compile
  1. Error ‘src/.objs/*.o file not recognized: File truncated’ occurs after the previous build is interrupted with a Control-C. The object file has zero length. Just delete that file and retry
5. cygport –debug engauge.cygport install (creates engauge-${VERSION}-1.x86_64/inst)
6. cygport –debug engauge.cygport package (creates engauge-${VERSION}-1.x86_64/dist/engauge/engauge-*.tar.xz)
# Cygwin SSH Key
1.	ssh-keygen … -C <email>
2.	ssh-keygen -e -f <privateKeyFileFromPreviousStep.pub>
Output file starts with ‘--- BEGIN SSH2 PUBLIC KEY ----’ and ends with ‘---- END SSH2 PUBLIC KEY ----'